Matrix of Alternatives to the Assignment Operators of Boost.Optional

    Deprecated functions of optional are not considered unless otherwise noted.
    * See Reference section for further explanation.
	optional	dual_optional	alt1_optional
Description	The current behaviour.	The same behaviour as optional, except for the following: / Given any instance o of type dual_optional<T&>, the semantics of o's operator= with operand rhs are such that: / if o is equal to none_t, then: / *o will be bound to the variable referenced by rhs if rhs were of type T&, / else *o will be bound to the variable referenced by *rhs if rhs were of type dual_optional<T&> and not equal to none_t. / if o is not equal to none_t, then: / *o will be assigned the value of rhs if rhs were of type T&, / else *o will be assigned the value of the variable referenced by *rhs if rhs were of type dual_optional<T&> and not equal to none_t. / if rhs were of type dual_optional<T&> and equal to none_t then the state of o will be modified such that it will equal none_t.	The same behaviour as optional except that the assignment operators for alt1_optional<T&> are disallowed.
Pros	1) For optional<T&>, the semantics of the two operator= are independent of the extant state of the operators' object(s). In other words, the said operators behave consistently w.r.t. to the extant state of their object(s).*	1) For dual_optional<T&>, the semantics of operator= are consistent with the semantics of assignment for the wrapped T&.*	1) We've avoided the controversy regarding the semantics of operator= in the case where T& is being wrapped.
Cons	1) For optional<T&>, the semantics of operator= are in some cases inconsistent with the semantics of assignment for the wrapped T&.*	1) For dual_optional<T&>, the semantics of the two operator= are dependent on the extant state of the operators' object(s). In other words, the said operators behave differently w.r.t. to the extant state of their object(s).*	1) Makes generic programming harder. Now alt1_optional<T-not-a-ref> and alt1_optional<T&> will have to be handled separately. / 2) Any class composing instances of alt1_optional<T&> cannot be used in stl-like containers. / 3) There is a loss of programmatic generality whenever a member variable is of type alt1_optional<T&>.

	alt2_optional	alt3_optional	alt4_optional
Description	The same behaviour as optional except that the assignment operators for alt2_optional<T> are disallowed.	The same behaviour as optional except that the assignment operators for alt3_optional<T> are disallowed but the deprecated reset methods of optional, which in general have not been considered, are allowed.	The same behaviour as optional except that alt4_optional<T&> will be disallowed altogether. Clients can use alt4_optional<reference_wrapper<T> > instead, since the latter type is semantically equivalent to the former type.
Pros	1) We've avoided the controversy regarding the semantics of operator= in the case where T& is being wrapped. / 2) Does not make generic programming harder.	1) We've avoided the controversy regarding the semantics of operator= in the case where T& is being wrapped. / 2) Does not make generic programming harder.	1) We've avoided the controversy regarding the semantics of operator= in the case where T& is being wrapped. / 2) The semantics of operator= for alt4_optional<reference_wrapper<T> > are not surprising w.r.t. to its wrapped type, since its wrapped type also rebinds on assignment.
Cons	1) Any class composing instances of alt2_optional<T> cannot be used in stl-like containers. / 2) There is a loss of programmatic generality whenever an instance of alt2_optional<T> is a member variable.	1) The only loss of programmatic generality is that any composing class of alt3_optional cannot be used in stl-like containers. / 2) The presence of reset methods, along with that of operator* and operator-> can mislead people to think that alt3_optional is just another smart pointer. Since smart pointers have shallow semantics for their reset methods, this may confuse people to think that alt3_optional also has shallow semantics for its reset methods, when it actually has deep semantics.

Reference

1. Optional
  1. Pros
    1. operator=(T const &)
      Let lhs be an instance of optional<T&>, and rhs an instance of T. In the case of lhs = rhs, *lhs will be bound to the rhs regardless of whether lhs is equal to none_t or not.
    2. operator=(optional const &)
      Let lhs, rhs be instances of optional<T&>. Consider the case of lhs = rhs:
      1. if rhs is not equal to none_t:
        then *lhs will be bound to *rhs regardless of whether lhs is equal to none_t or not.
      2. If rhs is equal to none_t:
        then the state of lhs will be modified such that it will be equal to none_t, regardless of whether lhs is equal to none_t or not.
    3. Conclusion
The semantics of operator= for any instance o of type optional<T&> are independent of the extant state of o.
  1. Cons
    1. operator=(T const &)
      Let lhs be an instance of optional<T&>, and rhs an instance of T. If *lhs is already bound to some instance of T, then “lhs = rhs” will rebind *lhs to rhs. Were lhs an instance of T& the latter behaviour would be inconsistent with the semantics of assignment for T&; and since lhs is just supposed to be a thin wrapper around T& (when it is not equal to none_t) then this behaviour may come as a surprise to some.
Example:
1. int x(10);
2. int & rx(x); //Binds rx to the variable x.
3. int y(100);
4. rx = y; // Assigns to the variable referenced by rx the value of the variable y.
5. optional<T&> ox(x); //Binds *ox to the variable x.
6. //Behaves like line 2.
7. ox = y; //Rebinds *ox to the variable y.
8. //Behaves unlike line 2.
    1. operator=(optional<T> const &)
      For any instances lhs, rhs of type optional<T&>, were both lhs and rhs not equal to none_t, then “lhs = rhs” has the semantics of rebinding *lhs to the variable referenced by *rhs. Were lhs and rhs instances of T& the latter behaviour would be inconsistent with the semantics of assignment for T&; and since lhs and rhs are just supposed to be thin wrappers around T& (when both are not equal to none_t) then this behaviour may come as a surprise to some.
      Example:
        1. int x(10);
        2. int y(11);
        3. int & rx(x); //Binds rx to the variable x.
        4. int & ry(y); //Binds ry to the variable y.
        5. rx = ry; //Assigns to the variable referenced by rx the value of the variable referenced by ry.
        6. //Hence x == 11.
        7. optional<T&> ox(x); //Binds ox to the variable x.
        8. //Behaves like line 3.
        9. optional<T&> oy(y); //Binds oy to the variable y.
        10. //Behaves like line 4.
        11. ox = oy; //Rebinds *ox to the variable referenced by *oy;
        12. //Behaves unlike line 5.
    1. Conclusion
      For any instance lhs of type optional<T&> that just acts as a thin wrapper around T&, and for any instance rhs of type T&, or of type optional<T&> that just acts as a thin wrapper around T&, the semantics of lhs = rhs are inconsistent with the semantics of assignment for T&.
2. Dual Optional
  1. Pros
    1. operator=(T const &)
      Let lhs be an instance of dual_optional<T&>, and rhs an instance of T.
      If *lhs is already bound to some instance of T, then “lhs = rhs” will assign to the variable referenced by *lhs the value of rhs. This is consistent with how assignment works for T&, and since in this case lhs is just a wrapper for T& such semantics is not surprising.
      If lhs is equal to none_t, then lhs = rhs will bind *lhs to rhs; this too is not surprising since that's the most reasonable choice.
      Example:
        1. int x(10);
        2. int & rx(x); //Binds rx to the variable x.
        3. rx = 11; //The variable referenced by rx is now assigned the value 11.
        4. dual_optional<int &> dox(x); //Binds *dox to the variable x.
        5. //Behaves like line 2.
        6. dox = 12; //The variable referenced by *dox is now assigned the value 12.
        7. //Behaves like line 3.
    1. operator=(dual_optional<T&> const &)
      Let lhs, rhs be instances of dual_optional<T&>.
      If *lhs, *rhs are already bound to some instances of T, then lhs = rhs will assign to the variable referenced by *lhs the value of the variable referenced by *rhs. Since in the latter case lhs and rhs are just wrappers around T&, the latter behaviour for operator= is not surprising given that it is in agreement with the semantics of the assignment for T&.
      If rhs is equal to none_t, then lhs = rhs will change the state of lhs so that it will be equal to none_t; this is not surprising since that's the most reasonable choice.
      If lhs and rhs are equal to none_t, then lhs = rhs is semantically a noop; this too is not surprising.
      Example:
    1. int x(10);
    2. int y(11);
    3. int & rx(x); //Binds rx to the variable x.
    4. int & ry(y); //Binds ry to the variable y.
    5. rx = ry; //Assigns the variable referenced by rx the value of the variable referenced by ry.
    6. //Hence x == 11.
    7. x = 10; //Reset x.
    8. optional<T&> ox(x); //Binds *ox the variable x. Behaves like line 3.
    9. optional<T&> oy(y); //Binds *oy to the variable y. Behaves like line 4.
    10. ox = oy; //Assigns to the variable referenced by *ox the value of the variable referenced by *oy.
    11. //Hence x == 11.
    12. //Behaves like line 5.
    1. Conclusion
      The semantics of operator= for dual_optional<T&> are consistent with the semantics of assignment for the wrapped T&.
  2. Cons
    1. operator=(T const &)
      Let lhs be an instance of dual_optional<T&>, and rhs an instance of T.
      If lhs is equal to none_t then “lhs = rhs” will bind *lhs to rhs.
      If lhs is not equal to none_t then “lhs = rhs” will assign to the variable referenced by *lhs the value referenced by rhs.
      Example:
    1. int x(10);
    2. int y(11);
    3. dual_optional<int &> ox;
    4. ox = x; //Binds *ox to the variable x.
    5. ox = y; //Assigns to the variable referenced by *lhs the value of the y.
    6. //Hence x == 11.
    7. //Behaves unlike line 4.
    Note that “ox = ...” has different semantics based on the extant state of ox.
    1. operator=(dual_optional<T&> const &)
      Let lhs, rhs be instances of dual_optional<T&> such that rhs is not equal to none_t.
      If lhs is equal to none_t then “lhs = rhs” will bind *lhs to the variable referenced by *rhs.
      If lhs is not equal to none_t then “lhs = rhs” will assign to the variable referenced by *lhs the value of the variable referenced by *rhs.
      Example:
    1. int y (11);
    2. int z(12);
    3. dual_optional<int &> oy(y);
    4. dual_optional<int &> oz(z);
    5. dual_optional<int &> lhs;
    6. lhs = oy; //Binds *lhs to the variable referenced by *oy.
    7. lhs = oz; //Assigns to the variable referenced by *lhs the value of the variable referenced by *oz.
    8. //Hence y == 12.
    9. //Behaves unlike line 6.
    Note that “lhs = ...” has different semantics based on the extant state of lhs.
    1. Conclusion
      operator= for dual_optional<T&> behave differently w.r.t. to the extant state of their object(s). This maybe surprising for some.